## Slide 1: PINT: Probabilistic In-band Network Telemetry
Ran Ben Basat, Harvard University
Joint work with Sivaram Ramanathan, Yuliang Li (Harvard), Gianni Antichi (QMUL), Minlan Yu, Michael Mitzenmacher (Harvard)
1
Notes: Hi Everyone, thanks for joining.
Today I’ll be presenting our probabilistic approach for in-band network telemetry.
And this work is really enabled by this new trend of programmable network components we are now seeing

## Slide 2: The rise of programmable devices
2
Notes: We have now programmable switches and smartnics from many different vendors,

## Slide 3
3
Programmable Data Planes: not an academic dream
Notes: But this is not just an academic game, we now have smartnics deployed in the public cloud

## Slide 4: Killer App: Network Telemetry
4
Tell me more about my packets.
  Is there a congestion/queue buildup?
  Do routing paths agree with the policy?
  Can flow increase its sending rate?
Notes: So, one of the selling point for these switches is the new and exciting telemetry capabilities.
And telemetry is about knowing my network status.
For example, we want to know if there’s a queue buildup somewhere that is causing congestion, if all routes agree with the policy (e.g., we may want all flows to go through a firewall), and we can even use telemetry to know whether a flow can safely increase its sending rate without causing congestion at any point.

## Slide 5: INT: In-band Network Telemetry
Add hop information (e.g., switch ID) onto the packet
INT metadata value
INT header
INT
Packet
Header
Packet Payload
INT Source
5
INT
INT header
INT metadata value
Packet Payload
Packet
Header
INT
Packet Payload
Packet
Header
INT
INT header
INT metadata value
Packet Payload
Packet
Header
INT header
INT metadata value
Notes: To that end, we have the INT, or In-band Network Telemetry, protocol.
The idea is conceptually simple. If we want to collect date from the network, we can just add it to data packets.
For example, say that we want to discover the path taken by a flow, i.e., collect the switch IDs along the path.
In this case, the first participating hop (which can be either the end host or an ingress switch), which is also called the INT source, adds a new INT header that tells all switches along the path which information we are collecting (i.e., the switch ID). It then adds its own ID, and send the packet to the next hop.

## Slide 6: INT: In-band Network Telemetry
Add hop information (e.g., switch ID) onto the packet
INT metadata value
INT header
INT
Packet
Header
Packet Payload
INT Source
6
INT
INT header
INT metadata value
Packet Payload
Packet
Header
INT
INT header
INT metadata value
Packet Payload
Packet
Header
INT
Packet Payload
Packet
Header
INT header
INT metadata value

## Slide 7: INT: In-band Network Telemetry
Add hop information (e.g., switch ID) onto the packet
INT metadata value
INT header
INT
Packet
Header
Packet Payload
INT Source
7
INT
INT header
INT metadata value
Packet Payload
Packet
Header
INT
INT header
INT metadata value
Packet Payload
Packet
Header
INT
Packet Payload
Packet
Header
INT header
INT metadata value
INT
Packet Payload
Packet
Header
INT header
INT metadata value
INT header
INT metadata value
Notes: The next hop reads the INT header, figures out we are collecting switch IDs, adds its own and forwards the packet.

## Slide 8: Telemetry Use case #1 – Congestion Control
State of the art: High Performance Congestion Control (HPCC, SIGCOMM 2019) is deployed in production in Alibaba.
8

## Slide 9: Telemetry Use case #2 – Path Discovery
Which path do my packets take?
Which rules do my packets follow?
Does the path conform with the operator’s policy?
9
Barefoot
Advanced Network Telemetry

## Slide 10: Telemetry Use case #3 – Network Debugging
Identify switches/links with high latency.
Discover load imbalance.
10

## Slide 11: INT: In-band Network Telemetry
INT is general
  Supports a large variety of functions including latency and buffer measurements.
  INT is deployed in major companies such as Alibaba in production.
But introduces high packet overheads.
  A single function (e.g., switch ID), adds 4 bytes per hop.
  Overhead grows multilinearly with the path length and number of collected telemetry types.
11
Notes: Add company icons
Discuss use cases here

## Slide 12: INT: In-band Network Telemetry
Issue III: High packet overheads degrade application performance.
12
Packet Payload
Packet
Header
INT
Packet Payload
Packet
Header
Without INT
With INT
Notes: Add company icons
Discuss use cases here

## Slide 13: INT Drawbacks
Issue III: High packet overheads degrade application performance.
13
Path Tracing
HPCC
Both
Notes: 5-hop, fat tree, 64 hosts, web search workload, all are standard

## Slide 14: INT Drawbacks
Issue III: High packet overheads degrade application performance.
Issue III: High packet overheads increase switch processing time.
Issue III: High packet overheads
14
I
Approximately 1% increase per telemetry type on 10G link
Payload
Payload
INT
Notes: Add company icons
Discuss use cases here

## Slide 15: INT Drawbacks
Issue III: High packet overheads impose severe collection costs.
Issue III: High packet overheads increase switch processing time.
  High network overheads.
  High processing overheads.
  State of the art telemetry processing (e.g., Confluo, NSDI 2019) rely on fixed byte-size data and are incompatible.
Issue III: High packet overheads
15
I
Notes: Add company icons
Discuss use cases here

## Slide 16: PINT: Probabilistic In-band Network Telemetry
Goal: encode telemetry information on packets while minimizing the bit-overhead.
Values: when a packet reaches switch , the switch observes a value .
Insight: most applications do not need all per-packet per-switch values, but aggregated data.
Implementation: P4 code.
16

## Slide 17: PINT: Probabilistic In-band Network Telemetry
Per-packet aggregation:
  For each , aggregate (e.g., max/min/sum/product) the values along its path.
Per-flow aggregation: For a flow with packets
  Static Case
  Dynamic Case: for each switch on the path, aggregate (e.g., estimate the median) over
17
: compute for each switch on the path.
Packets
Switches
Output
Per-packet
Output
Static Per-flow
Dynamic Per-flow
Notes: Visualize

## Slide 18: Techniques
Global hash functions allow implicit switch agreement, e.g., on the query type.
Approximations can reduce bit-overhead for numerical values.
Coding helps reduce spreading out static information on multiple packets.
18

## Slide 19: PINT solves the overhead issues
The lower overhead reduces the goodput degradation significantly.
By lowering the packet overhead, PINT reduces the switch processing time.
PINT produces less information with fixed-size packet digests and reduces the collection overheads.
19
Notes: Visualize

## Slide 20: Why should we use a probabilistic approach?
Reduces the bit-overhead added to packets, at the cost of approximation.
Different forms of approximation:
  Numerical approximation
    We mostly care about significant latencies or changes
  Requiring multiple packets
    Flows typically have multiple packets, and a few packets suffice for significant savings
20

## Slide 21: Use case 1: Congestion Control (per-packet aggregation)
The HPCC congestion control algorithm (SIGCOMM 2019) uses INT.
PINT moves the computation to the data plane to allow tracking just the maximum (i.e., the bottleneck).
PINT uses probabilistic rounding, to get the right signal in expectation.
PINT can probabilistically decide if to act on a packet.
21
Notes: "
HPCC computes what would be the rate that could cause congestion in each link along the path, and selects the best rate to avoid overloading the bottleneck.
We move the computation of the link sending-rate to the switches, which then allows us to store only the bottleneck’s statistics on the packet and not collect all the queueing statistics."
Then, when talking about the randomized rounding:
"We quantize the rate information into a small number of bits, probabilistically round the result so that the end-host will get the right sending rate in expectation. This means that a single packet may have slightly inaccurate feedback, but over multiple packets, this error cancels out and we converge to the right rates."
And when talking about the 1/16 sampling: "PINT may also use only some packets to deliver the feedback. The intuition is that we still get multiple feedbacks per RTT, which allows HPCC to work properly".

## Slide 22: Use case 2: Path Discovery (static per-flow aggregation)
Baseline solution: write a sampled ID on each packet.
  We can use the TTL field to get the hop number and run Reservoir Sampling (Sattari et al., 2010).
A
B
C
D
A Coupon Collector process. For hops it will take packets to detect the path.
C
A
A
D
A
C
B
22
Notes: RS allows us to get exact uniform distribution even though switches don’t know the path length
Static case is a generalization

## Slide 23: Coupon Collector Process
Number of samples
23
Notes: In some topologies, we may do better

## Slide 24: The power of Coding
24
A
B
The Baseline would:
Get information on the first packet.
Require 2 packets on average to get the second hop ID.
  Overall: packets in expectation.
Consider baseline sampling with probability 0.5, and writing otherwise.
If the first packet is an ID (e.g., ), we need more packets on average.
  Overall: packets in expectation.
𝐴⊕𝐵

## Slide 25: Path Profiling – the XOR algorithm
Assumptions:
  We know a “typical” length .
  Packets have unique identifiers.
Each switch XORs its identifier w.p. .
  Sample according to a global hash function
A
B
C
D
25

## Slide 26: Path Profiling – the XOR algorithm
Assumptions:
  We know a “typical” length .
  Packets have unique identifiers.
Each switch XORs its identifier w.p. .
  Sample according to a global hash function
A
B
C
D
26
Notes: ID can be 5-tuple / IPID / TCP seq / etc.

## Slide 27: Improving the Coupon Collector
27
Number of samples
Baseline
XOR
XOR

## Slide 28: Complete Algorithm
With probability , run the coupon collector algorithm.
Otherwise, choose one XOR layer at random.
The XOR instances have increasing probabilities.
Performance Guarantee: packets suffice.
Coupon collector
XOR1
XOR2
28
Notes: Add a results slide

## Slide 29: Also in the paper
Algorithms for dynamic aggregation.
Performance guarantees.
Support for concurrent queries.
29
Standalone
Concurrent
Standalone
Concurrent
Standalone
Concurrent

## Slide 31: Path Tracing
31

## Slide 32: Any Questions
32

## Slide 33: Any Questions

## Slide 34: Any Questions

## Slide 35: What to do?
Approximate Measurements
IEEE INFOCOM 20
IEEE/ACM ToN 19
ACM/IEEE ANCS 18
IEEE INFOCOM 18
IEEE INFOCOM 17
IEEE INFOCOM 16
…
Redesigning Algorithms for Speed
Leveraging Emerging Hardware Technologies
SIGMETRICS 2020
VLDB 2019
Designing Expressive Algorithms
IEEE ICNP 2018
This Talk
ACM SIGCOMM 19
IFIP NETWORKING 19
ACM CoNEXT 18
ACM ICDCN 18 best paper
IEEE MASCOTS 18
ACM SIGCOMM 17
IEEE INFOCOM 17
35

## Slide 36
Packet
Header
Packet Payload

## Slide 37: PISA Programmable Switch (Protocol Independent Switching Architecture)
1 | 2 | 3 | 4
1 | 0 | 1 | 0
Parser
1 | 2 | 3 | 4
1 | 2 | 3 | 4
Match-Action pipeline
Deparser
01011010…
01011010…
Stateful Memory
K1 | V1
K2 | V2
K3 | V3
1
K1 | V1
K2 | V2
K3 | V’
K4 | V”
K5 | V”
Notes: A brief overview of PISA switch…
Pipe goes one way. Once next stage, can’t go back. If you want to go back, may recirculate, but need to do again.
-> what is recirculation? Bring back… visit every stage a second time. Obviously it’s very expensive to do this for many packets, hurts throughput.
Recirculation: what we focus on today
PISA switch is real, “practical”, on the market, already widely used today in data centers (for quick iteration / deployment of new network functionality)
Barefoot Tofino.

## Slide 38: Database Queries in Spark
Multiple workers parallelize the data processing
Processing user-defined functions (UDFs) at workers
Worker
Data
UDF
User
Query
Query planner
Master Node
Plan
Switch
Query, UDF
Result
Data
38

## Slide 39: Database Queries in Spark
Multiple workers parallelize the data processing
Processing user-defined functions (UDFs) at workers
Worker
Data
UDF
User
Query
Query planner
Master Node
Plan
Switch
Query, UDF
Result
Data
39

## Slide 40: INT: In-band Network Telemetry
df
INT metadata value
INT header
INT
Packet
Header
Packet Payload
INT
Packet
Header
Packet Payload
INT header
INT Source
INT Target
INT
Packet
Header
Packet Payload
INT header
INT metadata value
INT
Packet
Header
Packet Payload
INT header
INT metadata value
40

## Slide 41
Query Planner
Spark Worker
Spark Master
Switch
Cheetah Worker
Cheetah Master
Pruned Entries
All Data
Packets
Unpruned Data
41

## Slide 43: INT: In-band Network Telemetry
df
INT
Packet
Header
Packet Payload
INT metadata value
INT header
43

## Slide 44: INT: In-band Network Telemetry
df
INT Source
INT
Packet
Header
INT header
INT metadata value
Packet Payload
INT
Packet
Header
INT header
Packet Payload
INT metadata value
INT Sink
44
Notes: BAK

## Slide 45: Also in the paper
Pruning algorithms for Join, Skyline, Groupby, Having, …
A network protocol that ensures reliability
Support for compound queries
Extensions to multiple switches and a DAG of tasks
45

## Slide 46: Path Profiling – the XOR algorithm
Assumptions:
  We know a “typical” length for some .
  Packets have unique identifiers.
Each switch XORs its identifier w.p. .
  According to a global hash function
A
B
C
D
46

## Slide 47: PISA Programmable Switch (Protocol Independent Switching Architecture)
Parser
K1 | V1
K2 | V2
K3 | V3
Deparser
K1 | V1
K2 | V2
K3 | V’
K4 | V”
K5 | V”
Notes: A brief overview of PISA switch…
Pipe goes one way. Once next stage, can’t go back. If you want to go back, may recirculate, but need to do again.
-> what is recirculation? Bring back… visit every stage a second time. Obviously it’s very expensive to do this for many packets, hurts throughput.
Recirculation: what we focus on today
PISA switch is real, “practical”, on the market, already widely used today in data centers (for quick iteration / deployment of new network functionality)
Barefoot Tofino.

## Slide 48: Network Operators Require Better Telemetry
48
Chart: 
| Category 4
Column2 | 4.3 | 2.5 | 3.5 | 4.5
Column3 | 2.4 | 4.4 | 1.8 | 2.8
Column4 | 2 | 2 | 3 | 5
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4
Series 1 | 4.3 | 2.5 | 3.5 | 4.5
Series 2 | 2.4 | 4.4 | 1.8 | 2.8
Series 3 | 2 | 2 | 3 | 5

## Slide 50: More bandwidth, faster computation
50

## Slide 51: Path Profiling – the XOR algorithm
Assumptions:
  We know a “typical” length .
  Packets have unique identifiers.
Each switch XORs its identifier w.p. .
  According to a global hash function
A
B
C
D
51

## Slide 53: Making more out of data
More complex/diverse queries
  Database queries
  Graph Mining
  Fine-grained Network Telemetry

## Slide 54: Key Challenges
Limited Amount of Fast Memory
Data Growth
Complex Queries
Limited Programmability
Real-time
Limited processing time

## Slide 55: Network Operators Require Better Telemetry
Networks become complex, making it hard to diagnose problems.
Self-driving networks require automatic understanding of the link bottlenecks and issues.
Attacks are becoming easy and affordable, which requires fine-grained traffic analysis to mitigate and secure.
55

## Slide 56
AD 2
AD 3

## Slide 57: Network Rates are on the Rise
The per-packet processing time is shrinking accordingly
57
Notes: Ethernet RFC (1984) sets MTU=1500B and is still the most common
Many packets – probabilistic algorithms

## Slide 58: What to do?
Approximate Measurement
Algorithms
IEEE INFOCOM 20
IEEE/ACM ToN 19
ACM/IEEE ANCS 18
IEEE INFOCOM 18
IEEE INFOCOM 17
IEEE INFOCOM 16
…
Redesigning Measurement for Speed
Leveraging Emerging Hardware Technologies
SIGMETRICS 2020
VLDB 2019
Designing Expressive Algorithms
IEEE ICNP 2018
ACM SIGCOMM 19
ACM IMC 19
IFIP NETWORKING 19
ACM CoNEXT 18
ACM ICDCN 18 best paper
ACM SIGCOMM 17
IEEE INFOCOM 17
…
58
Notes: Emphasize that these are my works
There are four directions that we should develop simultaneously and use depending on the use case.

## Slide 59: What to do?
Approximate Measurement
Algorithms
IEEE INFOCOM 20
IEEE/ACM ToN 19
ACM/IEEE ANCS 18
IEEE INFOCOM 18
IEEE INFOCOM 17
IEEE INFOCOM 16
…
Redesigning Measurement for Speed
Leveraging Emerging Hardware Technologies
SIGMETRICS 2020
VLDB 2019
Designing Expressive Algorithms
IEEE ICNP 2018
ACM SIGCOMM 19
ACM IMC 19
IFIP NETWORKING 19
ACM CoNEXT 18
ACM ICDCN 18 best paper
ACM SIGCOMM 17
IEEE INFOCOM 17
…
59
Notes: Emphasize that these are my works
There are four directions that we should develop simultaneously and use depending on the use case.

## Slide 60: Key Challenges
Limited Amount of Fast Memory
Data Growth
Complex Queries
Limited Programmability
Real-time
Limited processing time

## Slide 61: The end of the Software Approach
“By early 2020s”…
“with super-aggressive efforts, we'll get to the 3nm limit, where features are just 10 atoms across”
Paolo Gargini, Chairman of the IEEE International Roadmap for Devices and Systems
61
Notes: John Hennessy and David Patterson
ISCA 2018 Turing talk

## Slide 62: New Opportunities: Specialized Hardware
Specialized hardware to keep up with the data growth
GPU
FPGA
TPU
In this talk, we focus on programmable switches
  A customized ASIC for stream processing
62
Notes: Why switches, merge with 5?
Remove Harvard
Highlight ASIC

## Slide 63: Research Approach
Cheetah
PINT
Goal
Programming Abstraction
Algorithm Design
Prototype
Accelerating Databases
Collecting Telemetry Information
Pruning packets without affecting the output
Aggregating values observed by packets
Compressed history summarization on switch
Distributed encoding schemes
Notes: Think of challenges?
Change colors
Remove abstractions?

## Slide 64: Challenges of Running Algorithms on PISA
Constrained memory access:
  Partitioned between stages
  Can only R/W one address per stage
Computation: only basic arithmetic
Limited memory size, limited #stages
…
64
Notes:   Mention that the word size is ~8B
  Highlight in the previous slide
  Recirculation can help a lot (simplified operation in each pass), but hurts throughput
    Switch may have a small reserved capacity for recirc. No penalty.

## Slide 65: Today’s Agenda
Cheetah: Accelerating Database Queries with Switch Pruning
PINT: Probabilistic In-band Network Telemetry
Joint work with
Minlan Yu, Muhammad Tirmazi, and Jiaqi Gao (Harvard)
Joint work with
Minlan Yu, Michael Mitzenmacher, Shivaram Ramanathan, Yuliang Li (Harvard) and Gianni Antichi (QMUL)
65

## Slide 66: Example #1: Distinct Query
Selects all the distinct values
  E.g., SELECT DISTINCT seller FROM Products
Strawman solution: Bloom Filters
  Problem: have false positives which may drop distinct entries
But a cache works!
Our solution: Multi-row LRU cache
66
Notes:   Multi-row to reduce the number of per-packet comparison
  Implement LRU with a rolling replacement across stages

## Slide 67: Example #2: Top N
Compute the largest N entries in the queried column
  E.g., SELECT TOP 100 * FROM Products ORDER BY price
Strawman solution: Store the N largest so far
  Problem: N is often too large compared with the number of stages.
Our solution: Randomly partition the space
67

## Slide 68: The power of Coding
68
A
B
C
The Baseline would:
Get information on the first packet.
Require 1.5 packets on average to get the second hop ID.
Need 3 packets for sampling the last hop.
  Overall: packets in expectation.
Consider sampling with probability 0.5, and writing otherwise
If the first packet is an ID (e.g., ),
𝐴⊕𝐵⊕𝐶
𝐴⊕𝐵⊕𝐶

## Slide 69
Payload
Payload
INT

## Slide 70: This is food for researchers!
70
Notes: And this really allows us, as researchers, to do some really cool works and help many applications.

## Slide 71
Programmable Data Planes: not an academic dream
71
Notes: And major companies are buying programmable switches to replace traditional ones